# Attachment 7. Compliance List - Specifications for Infrastructure & e-Portal 2/2

# 1. Overall

# 1. NIC

# 1) NIC Overall

| No | Classification | Specification | Unit | Q'ty | Reference in proposal where this is covered |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | English version | Spanish version |
|  | e-Portal Hardware | H/W and S/W | Set | 1 |  |  |
| 1 | Innovation Center Operation Office | H/W and S/W | Set | 1 |  |  |
|  |  | Interior | Set | 1 |  |  |

# 2) e-Portal Hardware

| No | Equipment | Specification | Unit | Q'ty | Compliance (Y/N) Partially compliant | Bidder’s Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Web Server for users and administrator | 2U Rack Type 4 Core Intel Xeon 2.4GHz/10MB L3 Cache * 2EA Memory: 16GB HDD: 300GB 10K SAS * 2EA, RAID 1 HBA: 8Gb FC * 2EA LAN: 1Gbps Fiber Ethernet Card * 2EA ODD: DVD RW Dual Power Supply OS: Linux | Set | 3 |  |  |
| 2 | WAS Server | 2U Rack Type 4 Core Intel Xeon 2.4GHz/10MB L3 Cache * 2EA Memory: 16GB HDD: 300GB 10K SAS * 2EA, RAID 1 HBA: 8Gb FC * 2EA LAN: 1Gbps Fiber Ethernet Card * 2EA ODD: DVD RW Dual Power Supply OS: Linux | Set | 2 |  |  |
| 3 | LMS Server | 2U Rack Type 4 Core Intel Xeon 2.4GHz/10MB L3 Cache * 2EA Memory: 8GB HDD: 300GB 10K SAS * 2EA, RAID 1 HBA: 8Gb FC * 2EA LAN: 1Gbps Fiber Ethernet Card * 2EA ODD: DVD RW Dual Power Supply OS: Linux | Set | 1 |  |  |
| 4 | DB Server | 4U Rack Type 8 Core Intel Xeon 2.13GHz/24MB L3 Cache * 4EA Memory: 32GB HDD: 300GB 10K SAS * 2EA, RAID 1 HBA: 8Gb FC * 2EA LAN: 1Gbps Fiber Ethernet Card * 2EA ODD: DVD RW Dual Power Supply OS: Window Server 2008 R2 Enterprise | Set | 2 |  |  |
| 5 | LDAP Server | 2U Rack Type 4 Core Intel Xeon 2.4GHz/10MB L3 Cache * 2EA Memory: 8GB HDD: 300GB 10K SAS * 2EA, RAID 1 HBA: 8Gb FC * 2EA LAN: 1Gbps Fiber Ethernet Card * 2EA ODD: DVD RW Dual Power Supply OS: Linux | Set | 2 |  |  |
| 6 | Content and Uploading Server | 2U Rack Type 4 Core Intel Xeon 2.4GHz/10MB L3 Cache * 2EA Memory: 8GB HDD: 300GB 10K SAS * 2EA, RAID 1 HBA: 8Gb FC * 2EA LAN: 1Gbps Fiber Ethernet Card * 2EA ODD: DVD RW Dual Power Supply OS: Linux | Set | 1 |  |  |
| 7 | Search Engine Server | 2U Rack Type 4 Core Intel Xeon 2.4GHz/10MB L3 Cache * 2EA Memory: 8GB HDD: 300GB 10K SAS * 2EA, RAID 1 HBA: 8Gb FC * 2EA LAN: 1Gbps Fiber Ethernet Card * 2EA ODD: DVD RW Dual Power Supply OS: Linux | Set | 1 |  |  |
| 8 | CMS Server | 2U Rack Type 4 Core Intel Xeon 2.4GHz/10MB L3 Cache * 2EA Memory: 8GB HDD: 300GB 10K SAS * 2EA, RAID 1 HBA: 8Gb FC * 2EA LAN: 1Gbps Fiber Ethernet Card * 2EA ODD: DVD RW Dual Power Supply OS: Linux | Set | 1 |  |  |
| 9 | Media Server with VoD Transcoding | 2U Rack Type 4 Core Intel Xeon 2.4GHz/10MB L3 Cache * 2EA Memory: 8GB HDD: 300GB 10K SAS * 2EA, RAID 1 HBA: 8Gb FC * 2EA LAN: 1Gbps Fiber Ethernet Card * 2EA ODD: DVD RW Dual Power Supply OS: Linux | Set | 1 |  |  |
| 10 | SMS Server | 2U Rack Type 4 Core Intel Xeon 2.4GHz/10MB L3 Cache * 2EA Memory: 8GB HDD: 300GB 10K SAS * 2EA, RAID 1 HBA: 8Gb FC * 2EA LAN: 1Gbps Fiber Ethernet Card * 2EA ODD: DVD RW Dual Power Supply OS: Linux | Set | 1 |  |  |
| 11 | DBMS Server for Digital Repository System | 2U Rack Type 4 Core Intel Xeon 2.4GHz/10MB L3 Cache * 2EA Memory: 8GB HDD: 300GB 10K SAS * 2EA, RAID 1 HBA: 8Gb FC * 2EA LAN: 1Gbps Fiber Ethernet Card * 2EA ODD: DVD RW Dual Power Supply OS: Linux | Set | 1 |  |  |
| 12 | Web Analytic Server & Reporting Server | 2U Rack Type 4 Core Intel Xeon 2.4GHz/10MB L3 Cache * 2EA Memory: 8GB HDD: 300GB 10K SAS * 2EA, RAID 1 HBA: 8Gb FC * 2EA LAN: 1Gbps Fiber Ethernet Card * 2EA ODD: DVD RW Dual Power Supply OS: Linux | Set | 2 |  |  |
| 13 | Backup Server | 2U Rack Type 4 Core Intel Xeon 2.4GHz/10MB L3 Cache * 2EA Memory: 8GB HDD: 300GB 10K SAS * 2EA, RAID 1 HBA: 8Gb FC * 2EA LAN: 1Gbps Fiber Ethernet Card * 2EA ODD: DVD RW Dual Power Supply OS: Linux | Set | 1 |  |  |
| 14 | Mass Mail Server | Processor: Intel core i5-2400 processor (3.10 GHZ,6MB) and above Graphics: 1GB or above Memory: 6GB(DDR3 1333MHZ/4GB+2GB) HDD: 1TB(7200RPM S-ATA2) Monitor: 22" LCD Monitor O/S: Windows 7 Home Premium(64-bit) Keyboard: Spanish and English Mouse: USB Type Including Anti-Virus Program | Set | 1 |  |  |
| 15 | Backup Device | Backup methods LTO 5 Drives: 4 EA Slot: 48 or more Support capacity per: 1.5/3TB(uncompressed / compressed) Built-in Barcode Reader A variety of OS environments (Solaris, HP-UX, AIX, etc.) can be configured Including Cartridge 50Pack, FC Cable | Set | 1 |  |  |
| 16 | SAN Switch | Ports: 24 EA or more (Including SFP) Type of Port : Fiber Channel Interface(E_Port, F_Port, FL_Port, M_Port) Link speed: 8,4,2.1 Gbps auto-sensing Dual power supply & fan | Set | 2 |  |  |
| 17 | SAN Storage | Dual Active / Active configuration. Controller liver failure, fail-over support Offers more than 16GB of data cache Host Interface: 8Gbps FC 8 port, 1Gbps iSCSI 4 port Capacity: usable 20TB (900GB 2.5 in. 10k SAS HDD) RAID 0, 1, 5, 6, 10 support The major components (Power, Fan, Controller, etc.) redundancy | Set | 1 |  |  |
| 18 | NAS Storage | Dual Active / Active configuration. Controller liver failure, fail-over support Controller NAS: Per controller supports Controller FC: Per controller supports Offers more than 16GB of data cache NAS: Provides more than 72GB of data cache Host Interface: 8Gbps FC 8 port, 1Gbps iSCSI 4 port NAS interface 1Gbps 4 port, 10Gbps 4 ports provide more than Capacity : usable 24TB (900GB 2.5 in. 10k SAS HDD) RAID 0, 1, 5, 6, 10 support Storage virtualization can support The major components (Power, Fan, Controller, etc.) redundancy | Set | 1 |  |  |
| 19 | Monitoring PC | Processor: Intel core i5-2400 processor (3.10 GHZ,6MB) and above Graphics: 1GB or above Memory: 6GB(DDR3 1333MHZ/4GB+2GB) HDD: 1TB(7200RPM S-ATA2) Monitor: 22" LCD Monitor O/S: Windows 7 Home Premium(64-bit) Keyboard: Spanish and English Mouse: USB Type Including Anti-Virus Program | Set | 1 |  |  |
| 20 | L4 Switch | Layer 4~7 Switching Backplane: 16Gbps or more Concurrent Session: 4,000,000 or more 1G Fiber Ethernet: 8ports or more (Including SFP) | Set | 2 |  |  |
| 21 | Backbone Switch | 9slots chassis Backplane: 720Gbps or more Dual Switch Fabric Engine 10G Ethernet: 16ports or more 1G Fiber Ethernet: 24ports or more (Including SFP Cable) 10/100/1000 Mbps Ethernet: 48ports or more Dual Power Supply | Set | 2 |  |  |
| 22 | Workgroup Switch | Backplane: 32Gbps or more 1G Fiber Ethernet: 4ports or more (Including SFP) 10/100/1000 Mbps Ethernet: 24ports or more | Set | 2 |  |  |
| 23 | RACK | 42U Rack, PDU Only one(1) rack for KVM Switch, Panel Monitor | Set | 5 |  |  |
| 24 | Cable & Accessory for installation | Including cable & accessory for equipment installation | Set | 1 |  |  |

# 3) NIC Operation Office

- H/W and S/W

| No | Equipment | Specification | Unit | Q'ty | Compliance (Y/N) Partially compliant | Bidder’s Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Operator Computer | Processor: Intel core i5-2400 processor (3.10 GHZ,6MB) and above Graphics: 1GB and above Memory: 6GB(DDR3 1333MHZ/4GB+2GB) HDD: 1TB(7200RPM S-ATA2) Monitor: 22" LCD Monitor O/S: Windows 7 Home Premium (64-bit) Keyboard: Spanish and English Mouse: USB Type Including Anti-Virus Program | Set | 13 |  |  |
| 2 | Digital Copier | Color Print, Copy, Scan, Fax Printing Print Speed (Black): Up to 25 ppm Print Speed (Color): Up to 25 ppm Print Resolution (dpi): Up to 600 x 600 dpi Copy Copy Speed (Black): Up to 25 cpm Copy Speed (Color): Up to 25 cpm Copy Resolution: 600 x 600 dpi Scan Method: Color CCD or CIS or Flatbed Scan Speed: 20 ipm Resolution (Optical): 600 x 600 dpi Resolution (Enhanced): 4,800 x 4,800 dpi Fax Compatibility: ITU-T G3 General Interface: USB 2.0, Ethernet 10/100/1000 Base TX Memory: 1GB Including ADF | Set | 1 |  |  |
| 3 | Multi Function Color Printer | Color Print, Copy, Scan, Fax Printing Print Speed (Black): 21ppm Print Speed (Color): 21ppm Paper Input Capacity (Standard): 250 sheets Copy Copy Speed (Black): 21cpm Copy Speed (Color): 21cpm  Scan Method: Color CCD or CIS or Flatbed Scan Speed(Black): 11ipm or higher Fax Modem Speed (kbps): 33.6 Compatibility: ITU-T G3 Fax Memory: 4MB or up to 250pages General Interface: USB 2.0, Ethernet 10/100 Base TX Memory: 256MB | Set | 1 |  |  |
| 4 | UPS for PC | Output Capacity: 450Watts / 750 VA Max Configurable Power: 450 Watts / 750 VA Input /Output Voltage: 120V, 50/60Hz ± 3Hz Battery Type: sealed Lead-Acid battery Typical recharge time: 16hour Backup Time at Half Load: 11minute(225 Watts) Comply with electricity standards of Colombia | Set | 13 |  |  |
| 5 | Video Projector & Screen | Projector Native Resolution: XGA (1024x768) Brightness (ANSI-Lumens): 4000ANSI Contrast Ratio (FIFO): 2000:1 and above Lamp life (hours): 2500 and above Portable Screen Size: 120”(2400 x 1800) Material: Matt White | Set | 1 |  |  |
| 6 | DAS/NAS Storage for RIC content backup | 2.0GHz CPU, 512MB DDR2 Memory, 16MB Flash memory HDD: 8TB(4 X 2TB, 3.5" SATA) Tray: 4 X Hot Swappable Tray Network: 2 Gigabit Ethernet USB: 4 X USB 2.0 Form Factor: Tower | Set | 1 |  |  |
| 7 | Consumables & Stationery | Toner for Multifunction Color Printer (Black): 5EA Toner for Multifunction Color Printer (Yellow): 5EA Toner for Multifunction Color Printer (Magenta): 5EA Toner for Multifunction Color Printer (Cyan): 5EA Toner for Digital Copier (Black): 3EA Toner for Digital Copier (Yellow): 3EA Toner for Digital Copier (Magenta): 3EA Toner for Digital Copier (Cyan): 3EA | Set | 1 |  |  |
| 8 | Software | MS-Office, Home and Business | Set | 13 |  |  |
| 9 | Workgroup Switch | Backplane: 32Gbps or more 1G Fiber Ethernet: 4ports or more (Including SFP) 10/100/1000 Mbps Ethernet: 24ports or more | Set | 1 |  |  |
| 10 | Power & Network Cabling | Network Cabling(15 port): Cat 5 or 5e and miscellaneous materials Power Cabling: HIV 600 heat-resistant Cable and power plugs (Colombian standard Type) Comply with electricity/communication standards/regulations | Set | 1 |  |  |

- Interior

| No | Equipment | Specification | Unit | Q'ty | Compliance (Y/N) Partially compliant | Bidder’s Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Furniture | Office Desk: 13EA Partition: 1Set Chair: 21EA Printer Desk: 4EA Office Cabinet: 13EA Conference table(8 person): 1EA File Cabinet: 13EA * Reference only and minimum requirements | Set | 1 |  |  |
| 2 | Interior | Wall, Roof, Window, etc * The Bidder shall propose a space plan. | Set | 1 |  |  |

# 2. RIC

# 1) RIC Overall

| No | Classification | Specification | Unit | Q'ty | Reference in proposal where this is covered |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | English version | Spanish version |
| 1 | Server and Storage System | Hard ware & Soft ware | Set | 5 |  |  |
| 2 | RIC Operation Office | H/W and S/W | Set | 5 |  |  |
|  |  | Interior | Set | 5 |  |  |
| 3 | Multimedia Studio | H/W and S/W | Set | 5 |  |  |
|  |  | Studio Soundproof Construction | Set | 5 |  |  |
| 4 | Content Development and Research Office | H/W and S/W | Set | 5 |  |  |
|  |  | Interior | Set | 5 |  |  |
| 5 | Multimedia Classroom | H/W and S/W | Set | 10 |  |  |
|  |  | Interior | Set | 10 |  |  |
| 6 | General Classroom | H/W and S/W | Set | 10 |  |  |
|  |  | Interior | Set | 10 |  |  |
| 7 | RIC Security System | RIC Security System | Set | 5 |  |  |

# 2) Server and Storage system

- H/W and S/W

| No | Equipment | Specification | Unit | Q'ty | Compliance (Y/N) Partially compliant | Bidder’s Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Test Server | 2U Rack Type 4 Core Intel Xeon 2.4GHz/10MB L3 Cache * 2EA Memory: 8GB HDD: 300GB 10K SAS * 2EA, RAID 1 LAN: 1Gbps Fiber Ethernet Card * 2EA ODD: DVD RW Dual Power Supply OS: Linux | Set | 1 |  |  |
| 2 | Digital Resource Management Server | 2U Rack Type 4 Core Intel Xeon 2.4GHz/10MB L3 Cache * 2EA Memory: 8GB HDD: 300GB 10K SAS * 2EA, RAID 1 LAN: 1Gbps Fiber Ethernet Card * 2EA ODD: DVD RW Dual Power Supply OS: Linux | Set | 1 |  |  |
| 3 | DAS/NAS Storage | Processor: Intel Xeon Quad-Core Processor X3480 processor 3.06GHz+ Memory: 8192 MB DDR3 SDRAM HDD Bays: 16 * 3.5"/2.5" SATA III or SAS 6Gb/s Disk RAID Level: 0, 1, 5,6,10, 50,60 및 JBOD Interface: SATA/SAS (x16) via backplane Power: "Redundant power supply least 700W NIC: Intel 10GbE X520-DA2 Dual port with SFP GBIC Module HDD: 24TB (2,000GB 7.2K RPM SATA III Disk * 12EA) High Availability Support (HA) Access Guard: allows or denies specific IP or MAC addresses | Set | 1 |  |  |
| 4 | Workgroup Switch | Backplane: 32Gbps or more 1G Fiber Ethernet: 4ports or more (Including SFP) 10/100/1000 Mbps Ethernet: 24ports or more | Set | 7 |  |  |
| 5 | Rack | 42U Rack & KVM Switch, PDU, Panel Monitor | Set | 1 |  |  |

# 3) RIC Operation Office

- H/W and S/W

| No | Equipment | Specification | Unit | Q'ty | Compliance (Y/N) Partially compliant | Bidder’s Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Operator Computer | Processor: core i5-2400 processor (3.10 GHZ, 6MB) and above Graphics: 1GB or above Memory: 6GB(DDR3 1333MHZ/4GB +2GB) HDD: 1TB (7200RPM S-ATA2) Monitor: 22" LCD Monitor O/S: Windows 7 Home Premium (64-bit) Keyboard: Spanish and English Mouse: USB Type Including Anti-Virus Program | Set | 7 |  |  |
| 2 | Digital Copier | Color Print, Copy, Scan, Fax Printing Print Speed (Black): Up to 25 ppm Print Speed (Color): Up to 25 ppm Print Resolution (dpi): Up to 600 x 600 dpi Copy Copy Speed (Black): Up to 25 cpm Copy Speed (Color): Up to 25 cpm Copy Resolution: 600 x 600 dpi Scan Method: Color CCD or CIS or Flatbed Scan Speed: 20 ipm Resolution (Optical): 600 x 600 dpi Resolution (Enhanced): 4,800 x 4,800 dpi Fax Compatibility: ITU-T G3 General Interface: USB 2.0, Ethernet 10/100/1000 Base TX Memory: 1GB Including ADF | Set | 1 |  |  |
| 3 | Multi Function Color Printer | Color Print, Copy, Scan, Fax Printing Print Speed (Black): 21ppm Print Speed (Color): 21ppm Paper Input Capacity (Standard): 250 sheets Copy Copy Speed (Black): 21cpm Copy Speed (Color): 21cpm  Scan Method: Color CCD or CIS or Flatbed Scan Speed(Black): 11ipm or higher Fax Modem Speed (kbps): 33.6 Compatibility: ITU-T G3 Fax Memory: 4MB or up to 250pages General Interface: USB 2.0, Ethernet 10/100 Base TX Memory: 256MB | Set | 1 |  |  |
| 4 | Consumables & Stationery | Toner for Multifunction Color Printer (Black): 3EA Toner for Multifunction Color Printer (Yellow): 3EA Toner for Multifunction Color Printer (Magenta): 3EA Toner for Multifunction Color Printer (Cyan): 3EA Toner for Digital Copier (Black): 2EA Toner for Digital Copier (Yellow): 2EA Toner for Digital Copier (Magenta): 2EA Toner for Digital Copier (Cyan): 2EA | Set | 1 |  |  |
| 5 | UPS for PC | Output Capacity: 450Watts / 750 VA Max Configurable Power: 450 Watts / 750 VA Input /Output Voltage: 120V, 50/60Hz ± 3Hz Battery Type: sealed Lead-Acid battery Typical recharge time: 16hour Backup Time at Half Load: 11minute(225 Watts) Comply with electricity standards of Colombia | Set | 7 |  |  |
| 6 | Video Projector & Screen | Projector Native Resolution: XGA (1024x768) Brightness (ANSI-Lumens): 4000ANSI Contrast Ratio (FIFO): 2000:1 and above Lamp life (hours): 2500 and above Portable Screen Size: 120”(2400 x 1800) Material: Matt White | Set | 1 |  |  |
| 7 | Software | MS-Office, Home and Business | Set | 7 |  |  |
| 8 | Power & Network Cabling | Network Cabling (9 Port): Cat 5 or 5e and miscellaneous materials Power Cabling: HIV 600 heat-resistant Cable and power plugs of Colombian Type Compliant with Colombian electricity standards | Set | 1 |  |  |

- Interior

| No | Equipment | Specification | Unit | Q'ty | Compliance (Y/N) Partially compliant | Bidder’s Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Furniture | Office Desk: 7EA Partition: 1Set Chair: 15EA Printer Desk: 1EA Office Cabinet: 7EA Conference table(8person) 1EA File Cabinet: 7EA * Reference only and minimum requirements | Set | 1 |  |  |
| 2 | Interior | Wall, Roof, Window, etc Air Conditioner * The Bidder shall propose a space plan. | Set | 1 |  |  |

# 4) Multimedia Studio

- H/W and S/W

| No | Equipment | Specification | Unit | Q'ty | Compliance (Y/N) Partially compliant | Bidder’s Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | HD Camera System | HD Camera system Sensor: 1/3 Type 3Cmos Total pixels per sensor: 2.37 Mega pixels Effective pixels per sensor: 2.07 Mega-pixels Resolution: 1000 tv lines or more Zoom ratio: 18X Recording file format: MXF Recording format: MPEG 2 LONG GOP Recording frame rate: - 50Mbps: 1920 x 1080/60i,30p,24p; 1280x720/60p,30p, 24p - 35Mbps: 1920 x 1080/60i,30p,24p; 1280x720/60p,30p, 24p - 25Mbps: 1440 x 1080/60i,30p, 24p HD / SD-SDI OUTPUT: YES Time cord, Component Out function Including Battery Pack 2ea, Carrying case, Remote Controller, CF Card Reader, Rain Cover, Memory 32GB 2ea | Set | 2 |  |  |
| 2 | CCU for HD Camera System | Camera Control Unit Focus: Focus dial, Focus direction switch, Focus auto On / Off Key, Expanded focus key Iris: Iris dial, Iris direction switch, Iris auto On / Off key Zoom: Zoom lever, Zoom direction switch, Zoom Speed Switch White Balance: WHT BAL key, Preset key Gain: Gain key, Select Key Shutter: Shutter Key Camera control ch: 5ch | Set | 1 |  |  |
| 3 | W/L Microphone System for HD Camera | Transmitter Frequency response: 40 Hz ~ 18 KHz Audio input connector: 3-pole mini jack Receiver Frequency response: 40 Hz ~ 18 KHz Signal to noise ratio: 60dB or more *Proposed products shall have frequency range that is acceptable in Colombia. | Set | 1 |  |  |
| 4 | Boom Microphone System | Frequency Range: 20Hz - 20kHz Maximum SPL: 131dB SPL Sensitivity: -36.0dB re 1 Volt/Pascal Output: XLR Including Boom pole, Wind screen | Set | 1 |  |  |
| 5 | Tripod System | Tripod System for HD Camera with Prompter Head Payload range: 2 to 25kg / 4 to 55 lbs Counterbalance: 16 steps, plus Boost Button Tilt range: +90 ~ -70 For tripods with 100mm bowls Tripod Load Capacity: >40㎏ Weight: <2.6㎏ Min. Height: 460㎜ Max. Height: 1,550㎜ Material: Carbon fiber Spreader Load Capacity: >50㎏ Weight: < 0.8㎏ Cover Weight: < 3.81㎏ Material: Polyethylene Including Pan Bar, Dolly | Set | 1 |  |  |
|  |  | Tripod System for HD Camera only Head Counter balance: 5 + 0 Max. load: >4㎏ Pan angle range: 360deg Tilt angle range: > +90˚ to -75˚ Grade of drag: 3 and 0 Tripod interface: 75㎜ bowl Tripod Material: Dural aluminum Max. Height: >1,500㎜ Min. Height: <405㎜ Load Capacity: >20㎏ Spreader Load capacity: > 40㎏ Weight: < 0.6㎏ Including Dolly, Carrying Bag | Set | 1 |  |  |
| 6 | Studio LED Line Monitor | Screen Size: 42" Resolution: 1920 x 1080p Display Type: LED Aspect Ratio: 16:9 Including TV Stand | Set | 1 |  |  |
| 7 | Studio Monitor Speaker | Type: Bi-amp 2-way powered speaker Frequency response: 55Hz – 20kHz Output Power : 70W(Dynamic Power) | Set | 2 |  |  |
| 8 | Prompter | Display size: 20" (508mm) Brightness: 1000 Nits Resolution: 1280*1024 Contrast ratio: 1000:1 Input signal: BNC(Composite),VGA,SDI Reading Range: 7m(23ft) Including QStart Software, USB Shuttle Xpress Control | Set | 1 |  |  |
| 9 | Notebook for Prompter | CPU: Intel Core i5-560M (2.66GHz) Display: LED backlight / 13.3inch Panel resolution: 1366x768 HDD: 320GB Memory: 2GB DDR3 OS: Window 7 Professional Including DVD recorder, 6cell, 1Gbps LAN, 802.11n wireless LAN, HDMI, usb2.0 | Set | 1 |  |  |
| 10 | HD Switcher | Video Input - 8 simultaneous live video sources, in any combination of HD-SDI, HD Component, SD-SDI, SD Component, Y/C (BNC) or Composite connections and resolutions - Virtual: 8 independent Input Video Output: Up to 5 output connections and 2 independent A/V output signals - Mix and match output formats, connection types, resolutions and aspect ratios - HD-SDI, HD Component, SD-SDI, SD Component, Y/C (BNC) or Composite - HDMI, DVI and VGA output for displays or projector - Network output for live streaming Recording: Multi-track, multi-format recording of up to 8 simultaneous channels - Native recording in up to 1080p with time code Live Streaming: HD live streaming via Gigabit connection Audio Inputs: - 8 SDI Embedded - 8 AES3/EBU - 8 x 2 Balanced XLR (Microphone/Line) - Phantom Power Support Outputs: -3 SDI Embedded - 2 AES3/EBU - 4 Balanced XLR - 4 Balanced XLR (AUX) - 1 Stereo 1/4” (phones) Supported Formats: NTSC: 1080/30p, 1080/24p, 1080/60i, 720/60p, 720/30p, 720/24p, 480/60i Multi-Standard: NTSC-J; PAL 1080/25p, 1080/50i, 720/50p, 720/25p, 576/25i Playback Media Formats: AVI, DV, DVCPro, DVCProHD, FLV, F4V, H.263, H.264, MOV, MKV, MJPEG, MPEG (1, 2, all profiles, program or trans-port streams), MP4, WMV, WebM, PSD, PNG, TGA, BMP, JPEG, EXR, RAW, TIF, AIFF, MP3, WAV, (Including Apple ProRes) Processing: - Video: 4:4:4:4, 32-bit Floating Point - Audio: 4 channels, 96 kHz, 32-bit Floating Point Monitoring: Selectable layouts for user interface and multi-view preview displays | Set | 1 |  |  |
| 11 | Digital Video Deck | HD Format Connections SDI Video Input: 4 x 10-bit SD/HD/3 Gb/s SDI switchable SDI Video Output:4 x 10-bit SD/HD/3G Gb/s SDI switchable SDI Audio Input:16 channels embedded in SD and HD SDI Audio Output: 16 channels embedded in SD and HD Codec Support: Uncompressed QuickTime, Apple ProRes 422 (HQ) QuickTime, Avid DNxHD QuickTime, Avid DNxHD MXF 2K format support : 2048x1080p25 Displays: Built-in LCD for video, audio and time code monitoring Including SSD 128GB 2EA | Set | 2 |  |  |
| 12 | 2D/3D Non-Linear Editing System | Editing Software Premiere Pro CS6 Workstation MS Windows 7 Professional 64-bit OS E5-2640 2.50Ghz 15MB 1333MHz 6Core X 1EA Graphic : 1GB and above 16GB (4x4GB) DDR3 1000GB 1st HDD 1000GB 2nd HDD 16X DVD+-RW Super Multi SATA 1st Drive USB Standard Keyboard 22 inch monitor 2EA Storage Host Interface: Dual 4Gb Fiber Channels Type: Single RAID Controller CPU: Intel Xscale i80348@800Mhz RAID level: 0, 1, 10, 3, 5, 6 , 30, 50, 60 , Single Disk and JBOD Bay: Hotswap 8ea Capacity : 16TB(2,000GB X 8EA) HDD: Option(SATAII,SATA,ATA) Cache: Standard 1GB Power: Redundant by Dual 460W Power modules Module - Drive Tray X 8EA Embedded Web browser-based RAID manager | Set | 1 |  |  |
| 13 | LCD Multi-view Monitor | Screen Size: 42" Resolution: 1920 x 1080p Display Type: LED Aspect Ratio: 16:9 Including TV Stand | Set | 1 |  |  |
| 14 | PGM Monitor | Size: 17inch Resolution: 1366X768 Contrast ratio: 900:1 Input: 2 X HD/SD SDI, 1xDVI, Analog Component / Composite / S-video / RGB Output: 1 X HD/SD SDI through-out | Set | 1 |  |  |
| 15 | HDV VTR | Recording format: HDV1080/60i, 1080/50i, 1080/24p, 1080/25p, 1080/30p Playout format: HDV1080/60i, 1080/50i, 1080/24p, 1080/25p, 1080/30p. Video input/output: BNC x1/BNC x1 S-video input/output: Mini-DIN 4pin x 2 Component video output: BNC x 3 Digital uncompressed output: HDMI Connector x 1 Audio input: RCA x2, Stereo / Audio output: RCA x2,stereo LCD monitor: 2.7-inch type | Set | 1 |  |  |
| 16 | Sync Generator | HD Sync: Tri-level SD Sync: Color Black, 75% Color Bars Accuracy: 3 ppm User Controls: External Dipswitch | Set | 1 |  |  |
| 17 | Brue Ray Player | Video Out: 1.0 V (p-p), 75 Ω, sync negative, RCA jack x 1 HDMI out: 19 pin (Type A, HDMI™ Connector) | Set | 1 |  |  |
| 18 | HD-SDI Router | Port: 8 Input / 8 Output Signal: 10 Bit SD-SDI, HD-SDI, 3G-SDI Video Rate: 270 Mb/s ~ 3 Gb/s Connector: BNC Jack, 75 Ohms Audio: Embedded, TV Standard 48KHz 24Bit Sampling | Set | 1 |  |  |
| 19 | Audio Distribution AMP | Input Number of Input:1In ( 2 Channels L/R) Impedance: 600 ohm or 20K ohm balanced  Output Number of Output: 6 Out ( 2 Channels L/R) Loop Output: 1 Out (2 Channels L/R) Impedance: 600 ohm balanced Output | Set | 1 |  |  |
| 20 | Interactive Display Board | Size: 82", 16:9 aspect ratio Resolution: 1920×1080P, Full HD Brightness: 450(cd/㎡) Support multi touch gestures, Soft Key function Recognition Speed: 125fps Plug and Play(USB 2.0) Including cables and accessories, S/W | Set | 1 |  |  |
| 21 | Audio Mixer | 16ch digital audio mixer Chanel: 1~16 Microphones/Lines Analog input CH Input 1 to 12: Microphones & Lines CH Input 13 to 16: Lines 2 TR In [L, R]: 600Ω Lines Analog Output Stereo Out [L,R]: 600Ω Lines Omni Out(1 to 4): 10KΩ Lines Monitor Out(L,R): 10KΩ Lines 2TR out (L,R): 10KΩ Lines Digital Input 2TR IN Digital: RCA Pin Jack ADAT In: Optical Digital Output 2TR Out Digital: RCA Pin Jack ADAT Out: Optical | Set | 1 |  |  |
| 22 | Control Room Monitor Speaker | Type: Bi-amp 2-way powered speaker Frequency response: 55Hz – 20kHz Output Power : 70W(Dynamic Power) | Set | 2 |  |  |
| 23 | Wired Microphone | Pick-up pattern: cardioid Frequency response: 80 – 15,000 Hz Sensitivity (free field, no load, 1 kHz): 1.5 mV/Pa Nominal impedance: 350 Ω Min. terminating impedance: 1 kΩ Including Stand | Set | 2 |  |  |
|  | Gooseneck Microphone | Polar Pattern: Hyper-cardioid Frequency response: 70 Hz - 18 kHz Maximum Sound Level: 124 dB SPL Connector: XLR-3 male Equivalent Acoustic Noise: 39 dBA SPL Including Stand | Set | 1 |  |  |
| 24 | W/L Microphone | Frequency response: 25~18000Hz Receiver Antenna connector: 2x BNC Audio output level (balanced): XLR Transmitter RF output power typ. 30 mW Power supply 2x AA batteries Microphone Transducer principle : condenser AF sensitivity: 20 mV/Pa omni directional Sound pressure level (SPL): 130 dB(SPL) max. *Comply with frequency rate of Colombia | Set | 2 |  |  |
| 25 | Headphone | System: Dynamic Frequency range: 12Hz to 28kHz Sensitivity: 125dB SPL/V Input impedance: 32 Ohms Max. input power: 30mW Cable: 1m cable | Set | 1 |  |  |
| 26 | Network Switch | Connectors: 16 10BASE-T/100BASE-X/1000BASE-T, 4 Gigabit SFP ports Performance: 40 Gbps switching capacity, max. / 29.6 Mpps forwarding rate, max | Set | 1 |  |  |
| 27 | Intercom System | Panel Microphone Input Type: Electret Headset Microphone Input Type: Dynamic Speaker Output - Load Impedance: >= 4Ω - Frequency Response(Panel Mic): 600 - 10KHz ± 3dB Including Headset 3EA, Belt-pack 2EA | Set | 1 |  |  |
| 28 | Back-up System | LTO Backup system Sustained Transfer Rate - 100MB/s direct attached, - up to 75 MB/s network Hard Disk Drive - 2000 GB X 2 – RAID0/1 Format Compatibility - GNU or POSIX tar v1.20 or later, LTFS 2.0 Direct Attached File Systems Supported Drive - Native Capacity: 1500 GB - Average Access Time: 52 Sec from BOT - Rewind Time: 96 Sec from EOT - Average Load Time: >19 Seconds - MTBF: 250,000 Hours - Uncorrected Error Rate: 1x1017 LTO 5 Media - Archival Life — 30 years - Durability — 5,000 load/unload cycles Including LTO5 1.5TB Tape 10ea, Cleaning tape 1ea, Rack mount Kit | Set | 1 |  |  |
| 29 | On Air Lamp | Lamp Type: Red LED Type Tally Input: 10mA | Set | 2 |  |  |
| 30 | UPS | Output Power Capacity: 10 KVA Input - Voltage Range: 90~130AVC - Frequency: 50/60Hz ± 5% - Max Input Current: 112A Output - Voltage Range: 110AVC± 1% - Frequency: 50/60Hz ± 5% - AVR Function: included Battery Type Maintenance-free sealed Lead-Acid battery Typical recharge time: 90% capacity after 8 hours Surge Protection Backup Time: 30 minutes or less Comply with electricity standards of Colombia | Set | 2 |  |  |
| 31 | Chroma key Screen | 150” Electronic Screen 3000 X 4000 (mm) Color: Blue | Set | 1 |  |  |
| 32 | Console Desk | Material: Wood and Steel Number of Bay: 5 Bay Base: Rack Type | Set | 1 |  |  |
| 33 | NLE Desk | Material: Wood desk for 2D/3D Editing System | Set | 1 |  |  |
| 34 | Power Distributer | AC Voltage meter: Line input / output (use of the voltage) Channel: 8 Ch Ch load: 10A or more Total max load: 45A or more Power: 55 watts or more Comply with electricity standards of Colombia | Set | 2 |  |  |
| 35 | System Rack | 19", 42U Aluminum | Set | 1 |  |  |

- Studio Soundproof Construction

| No | Equipment | Specification | Unit | Q'ty | Compliance (Y/N) Partially compliant | Bidder’s Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Soundproof Interior | Soundproof system and doors, dustproof system, Furniture Air conditioner 2 Set or more Extinguishing System: Carbon Dioxide Extinguishing System or Halogen Compounds Extinguishing System * Reference only – The Bidder shall propose an optimized space plan. * Comply with electricity standards of Colombia | Set | 1 |  |  |
| 2 | Power Cabling and Installation | Electric Power Cabling Audio/Visual Signal Cabling Equipment Installation * For Audio/Visual Signal Cabling, Cables and connectors from "Beldon" or "Gepco" are advised. * Comply with electricity standards of Colombia | Set | 1 |  |  |
| 3 | Studio Lighting | Light Fly Duct: 5000L 4EA Upper Horizon Light: 300W 9EA Spot Light: 650W, 3EA Back Spot Light: 2EA Photo Optic Light(POL 4/220W): 10EA Barn Door: 3EA Light Hanger: 24EA Safety Chain: 24EA R/D Unit Panel & Control Board(12RD) Pipe Grid * Reference only – The Bidder shall propose an optimized space plan. *Proposed lightings shall be low-heat emitting products. *Comply with electricity standards of Colombia | Set | 1 |  |  |

# 5) Content Development and Research Office

- H/W and S/W

| No | Equipment | Specification | Unit | Q'ty | Compliance (Y/N) Partially compliant | Bidder’s Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Operator Computer | Processor: Intel core i5-2400 processor (3.10 GHZ,6MB) and above Graphics: 1GB or above Memory: 6GB(DDR3 1333MHZ/4GB +2GB) HDD: 1TB (7200RPM S-ATA2) Monitor: 22" LCD Monitor * 2EA O/S: Windows 7 Home Premium(64-bit) Keyboard: Spanish and English Mouse: USB Type Including Anti-Virus Program | Set | 10 |  |  |
| 2 | Multi Function Color Printer | Color Print, Copy, Scan, Fax Printing Print Speed (Black): 21ppm Print Speed (Color): 21ppm Paper Input Capacity (Standard): 250 sheets Copy Copy Speed (Black): 21cpm Copy Speed (Color): 21cpm  Scan Method: Color CCD or CIS or Flatbed Scan Speed(Black): 11ipm or higher Fax Modem Speed (kbps): 33.6 Compatibility: ITU-T G3 Fax Memory: 4MB or up to 250pages General Interface: USB 2.0, Ethernet 10/100 Base TX Memory: 256MB | Set | 2 |  |  |
| 3 | UPS for PC | Output Capacity: 450Watts / 750 VA Max Configurable Power: 450 Watts / 750 VA Input /Output Voltage: 120V, 50/60Hz ± 3Hz Battery Type: sealed Lead-Acid battery Typical recharge time: 16hour Backup Time at Half Load: 11minute(225 Watts) Comply with electricity standards of Colombia | Set | 10 |  |  |
| 4 | Digital Copier | Color Print, Copy, Scan, Fax Printing Print Speed (Black): Up to 25 ppm Print Speed (Color): Up to 25 ppm Print Resolution (dpi): Up to 600 x 600 dpi Copy Copy Speed (Black): Up to 25 cpm Copy Speed (Color): Up to 25 cpm Copy Resolution: 600 x 600 dpi Scan Method: Color CCD or CIS or Flatbed Scan Speed: 20 ipm Resolution (Optical): 600 x 600 dpi Resolution (Enhanced): 4,800 x 4,800 dpi Fax Compatibility: ITU-T G3 General Interface: USB 2.0, Ethernet 10/100/1000 Base TX Memory: 1GB Including ADF | Set | 1 |  |  |
| 5 | Digital Camera | Effective Pixel: Approx. 20.3 Mega-pixels Total Pixel: Approx. 21.6 Mega-pixels Image Sensor Type: CMOS Main LCD Screen: AMOLED Resolution: VGA ( 640X480 ) 614k dots USB 2.0 (HI-SPEED) Video Out: NTSC, PAL (user selectable), HDMI 1.4a: (1080i, 720P, 576P / 480P) Storage media: SD / SDHC / SDXC Including Tripod, Rechargeable Battery, Bag, Lens(18~55mm Lens), 32GB Memory card, Compatible Microphone | Set | 2 |  |  |
| 6 | HD Camcorder | Type: 1080p HD Switch Grip Camcorder Lens: Optical Zoom: 20x, Digital Zoom: 40x No. of Pixels: 5.1M Pixel Sensor Type: 1/4" (effec.1/6.3") Display: 2.7" Wide touch Recording Format: H.264 HP Resolution: Full HD i (1920x1080/60i), Vertical HD(1920x1080/30p), HD p (1280x720/60p) SD D1 (720x480/60P) Video File Format: MP4 Audio Recoding Format: AAC Storage media: SD / SDHC / SDXC including Tripod, Bag, 32GB Memory card | Set | 2 |  |  |
| 7 | Video Projector & Screen | Projector Native Resolution: XGA (1024x768) Brightness (ANSI-Lumens): 4000ANSI Contrast Ratio (FIFO): 2000:1 and above Lamp life (hours): 2500 and above Portable Screen Size: 120”(2400 x 1800) Material: Matt White | Set | 1 |  |  |
| 8 | Consumables & Stationery | Toner for Multifunction Color Printer (Black): 5EA Toner for Multifunction Color Printer (Yellow): 5EA Toner for Multifunction Color Printer (Magenta): 5EA Toner for Multifunction Color Printer (Cyan): 5EA Toner for Digital Copier (Black): 3EA Toner for Digital Copier (Yellow): 3EA Toner for Digital Copier (Magenta): 3EA Toner for Digital Copier (Cyan): 3EA | Set | 1 |  |  |
| 9 | CD/DVD Duplicator | 1:11 Duplication Memory: 128MB Internal HDD: 500GB Reader: 18X DVD Rom Writer: 24X DVD Recorder * 11 Disk Writing Speed: DVD+R 24X / DVD-R 24X / CD-R 48X / DVD+RW 8X / DVD-RW 6X / CD-RW 32X Stand alone type | Set | 1 |  |  |
| 10 | CD/DVD Printer | Supported Media: CDs, DVDs, Blu-ray Discs, and HD-DVDs Disc Input: 100 Printing Technology: Inkjet printer Print Resolution: 4800 dpi x 1200dpi Connectivity: Hi Speed USB Including Label Design S/W | Set | 1 |  |  |
| 11 | DAS /NAS Storage for RIC content backup | 2.0GHz CPU, 512MB DDR2 Memory, 16MB Flash memory HDD: 8TB(4 X 2TB, 3.5" SATA) Tray: 4 X Hot Swappable Tray Network: 2 Gigabit Ethernet USB: 4 X USB 2.0 Form Factor: Tower | Set | 1 |  |  |
| 12 | Software | MS-Office, Office University 2010 | Set | 10 |  |  |
|  |  | Creative Suite 6 Design & Web Premium Student and Teacher Edition | Set | 2 |  |  |
|  |  | Creative Suite 6 Production Premium Student and Teacher Edition | Set | 2 |  |  |
|  |  | Creative Suite 6 Master Collection Student and Teacher Edition | Set | 2 |  |  |
|  |  | Autodesk 3D Max Design 2013, Subscription (1 year) | Set | 1 |  |  |
|  |  | Corel painter 12 | Set | 2 |  |  |
|  |  | CorelDRAW Graphics Suite X6 | Set | 2 |  |  |
|  |  | Sound Forge Pro 10 | Set | 2 |  |  |
| 13 | Blank DVD | DVD-R, 4.7GB 16X 50P, Printable | Set | 800 |  |  |
| 14 | Power & Network Cabling | Network Cabling(14 Port): Cat 5 or 5e and miscellaneous materials Power Cabling: HIV 600 heat-resistant Cable and power plugs of Colombian Type Comply with electricity standards of Colombia | Set | 1 |  |  |

- Interior

| No | Equipment | Specification | Unit | Q'ty | Compliance (Y/N) Partially compliant | Bidder’s Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Furniture | Office Desk: 10EA Partition Chair: 18EA Printer Desk: 2EA Office Cabinet: 8EA Conference table(8person) 1EA File Cabinet: 10EA * Reference only and minimum requirements | Set | 1 |  |  |
| 2 | Interior | Wall, Roof, Window, etc Air Conditioner *The Bidder shall propose a space plan. | Set | 1 |  |  |

# 6) Multimedia Classroom

- H/W and S/W

| No | Equipment | Specification | Unit | Q'ty | Compliance (Y/N) Partially compliant | Bidder’s Comments |
| --- | --- | --- | --- | --- | --- | --- |
|  | A. Electronic Desk Board |  |  |  |  |  |
| 1 | PC for Trainer | Processor: Intel core i5-2400 processor(3.10 GHZ,6MB) and above Graphics: 1GB or above Memory: 6GB(DDR3 1333MHZ/4GB +2GB) HDD: 1TB (7200RPM S-ATA2) Monitor: 22" LCD Monitor O/S: Windows 7 Home Premium(64-bit) Keyboard: Spanish and English Mouse: USB Type Including Anti-Virus Program & HD Encoder | Set | 1 |  |  |
| 2 | PC for Trainee | Processor: Intel core i5-2400 processor(3.10 GHZ,6MB) and above Graphics: 1GB or above Memory: 6GB(DDR3 1333MHZ/4GB +2GB) HDD: 1TB (7200RPM S-ATA2) Monitor: 22" LCD Monitor O/S: Windows 7 Home Premium(64-bit) Keyboard: Spanish and English Mouse: USB Type Including Anti-Virus Program | Set | 30 |  |  |
| 3 | Multi Function Color Printer | Color Print, Copy, Scan, Fax Printing Print Speed (Black): 21ppm Print Speed (Color): 21ppm Paper Input Capacity (Standard): 250 sheets Copy Copy Speed (Black): 21cpm Copy Speed (Color): 21cpm  Scan Method: Color CCD or CIS or Flatbed Scan Speed(Black): 11ipm or higher Fax Modem Speed (kbps): 33.6 Compatibility: ITU-T G3 Fax Memory: 4MB or up to 250pages General Interface: USB 2.0, Ethernet 10/100 Base TX Memory: 256MB | Set | 2 |  |  |
| 4 | Software | MS-Office, Office University 2010 | Set | 31 |  |  |
| 5 | e-Podium | Type: Stand Type Top unit equipped with a minimum 21” writable LCD touch monitor. PC and monitor locking system to prevent theft. Built-in board cable and microphone Including Gooseneck Microphone, content authoring S/W * This product shall come form the same manufacturer of the Interactive Display Board. | Set | 1 |  |  |
| 6 | Interactive Display Board | Size: 70", 16:9 aspect ratio Resolution: 1920×1080P, Full HD Brightness: 450(cd/㎡) Support multi-touch gestures, soft key function Recognition Speed: 125fps Plug and Play(USB 2.0) Including cables and accessories, S/W | Set | 1 |  |  |
|  | B. Audio System |  |  |  |  |  |
| 1 | Wireless Microphone | Handheld Transmitter Audio Input Level: +2 dBV maximum at -10dB position Gain Adjustment Range: 10dB RF Transmitter Output: 30mW Maximum Battery Life 8 hours (alkaline) Including Microphone Receiver: XLR connector (into 600 Ω load): –13 dBV XLR Out: Impedence balanced Including external power supply *Comply with frequency rate of Colombia | Set | 2 |  |  |
| 2 | Wired Microphone | Type: Dynamic Frequency Response: 50 to 15,000 Hz Polar Pattern: Cardioid Sensitivity: –54.5 dBV/Pa (1.85 mV) Including 10m Cable | Set | 2 |  |  |
| 3 | DSP Mixer | Acoustical Echo Cancellation Noise Cancellation Built-in telephone interface and 35W power amplication Audio Performance Frequency Response: 20Hz to 22KHz ±1dB Dynamic Range: 105dB(non A-weighted) Matrix Mixing Parameters 12 analog in/out 18 expansion bus in/out 8 assignable processing blocks in/out 4X35W speaker amplication 1 telco input/1 telco out Control 10/100 Mbps Ethernet Network Port and PC Port RS-232(DB-9 female) USB 2.0 compatible Including Configuration and Admin Software | Set | 1 |  |  |
| 4 | Ceiling Speaker | Frequency range (-10 dB): 80 Hz - 20 kHz Power handling (pink noise): 20 W Sensitivity: 86 dB, 1 W @ 1 m, 1/2 space Nominal impedance: 8 Ω | Set | 8 |  |  |
|  | C. Video System |  |  |  |  |  |
| 1 | HD Matrix Switcher | RGBHV+Stereo, 8in 8out RS-232 Control Audio Input Level(max): +14dBu, unbalanced Input Impedence: 18KΩ Output Level(max): +14dBu, unbalanced Output Impedence: 50Ω Connectors: 3T Wideband Video Input Level(max): +/- 1.5V Input Impedence: 75Ω Frequency Response: 300MHz or more (+/- 3dB) HV Sync Input Level(max): +/- 5V HV Sync Output Level(max): +/- 5V Connectors: HD-15 | Set | 1 |  |  |
| 2 | Visual Presenter | Capture area : 420 x 336(mm) Focus : Auto / Manual Camera Module: 42X Zoom, 1,300,000 pixels Input: VGA(15pin D-Sub Output: VGA(15pin D-Sub), DVI Interface: RS-232C, USB, SD Memory | Set | 1 |  |  |
| 3 | Video Conference System | Video Standards and Protocols H.264 / H.263++ / H.261 / H.239 / People+Content / H.263 & H.264 Video Error Concealment People Video Resolution 720p, 30fps at 1 Mbps–2 Mbps 4SIF (704 x 480)/4CIF (704 x 576) at 256 Kbps-2 Mbps SIF (352 x 240), CIF (352 x 288) QSIF (176 x 120), QCIF (176 x 144) Content Video Resolution Up to 720p Input: SXGA (1280x1024), XGA (1024 x 768),SVGA (800 x 600), VGA (640 x 480) Output: XGA (1024x768), SVGA (800x600) Audio Standards and Protocols Stereo Surround 22 kHz bandwidth 14 kHz bandwidth, G.722.1 Other ITU-Supported Standards H.221 communications H.224/H.281 far-end camera control H.323 Annex Q far-end camera control H.225, H.245, H.241, H.331 H.239 dual stream H.231 in multipoint calls H.243 chair control H.460 NAT/firewall traversal BONDING, Mode 1 including document share function | Set | 1 |  |  |
| 4 | Camera | PTZ Camera Image device: 1/3 type, CMOS Video signal: 1080/59.94i, 1080/50i. 1080/29.97p, 1080/25p, 720/59.94p,720/50p/720/29.97p,720/25p ntsc/pal Lens: 10x optical/ 4x digital Video out: HD-SDI, Analog Component | Set | 2 |  |  |
| 5 | Motion Detection Camera System | Sensor Camera CCD Fix Type Camera 1/3” High Resolution CCD Total Pixels: 811(H)x506(V) Effective Pixels: 768(H)x494(V) Resolution: More than 630TV Lines Motion Tracking Controller E6600CPU, 1GB SDRAM, 120GB HDD, Composite Video Input, Rack Type Motion tracking Control H/W RS-232C, USB interface Including Cam Motion S/W | Set | 1 |  |  |
| 6 | Monitor | Screen Size: 42" Resolution: 1920 x 1080p Display Type: LED 4 HDMI port Including Ceiling Type Bracket | Set | 2 |  |  |
|  | D. Classroom Control |  |  |  |  |  |
| 1 | Controller | 7 Configurable RS-232 / RS-422 / RS-485 Serial ports 8 Relays 8 IR / Serial ports 8 Digital I/O ports 2 Communication Networks: AxLink and Ethernet (TCP/IP) 404 MIPS processor speed 64 MB RAM or 256 MB RAM 2 GB CompactFlash 1 MB Non-Volatile Memory | Set | 1 |  |  |
| 2 | Lecture Touch Control Panel | Compact 4.3" size 16x9 WQVGA color display Screen resolution (HV): 480 x 272 pixels Available in a high-gloss and textured matte combination finish in your choice of black or white Power over Ethernet (PoE) 128 MB Standard memory / 256 MB Flash memory 1 capacitive-touch external button | Set | 1 |  |  |
| 3 | Wireless Touch Panel | Retina display 9.7-inch (diagonal) LED-backlit glossy widescreen Multi-Touch display with IPS technology 30-pin dock connector port 3.5-mm stereo headphone minijack Built-in speaker Microphone | Set | 1 |  |  |
| 4 | iPad License | Administrators shall be able to control and manage the equipment through iPad. | Set | 1 |  |  |
| 5 | Program Fee | Audio/Visual equipment on/off control Camera Pan/Tilt/Zoom control Signal input/output control through HD Matrix Switcher and DSP Mixer | Set | 1 |  |  |
| 6 | Classroom Management S/W | 1 Teacher and 30 Student License Recovery management function System recovery/Existing status store Reserved recovery set-up Recovery install/delete PC management function Screen lock/unlock Internet lock/unlock Registry lock/unlock Task management lock/unlock Program execution lock/unlock Instruction tool Sending message Sending notice message Remote execution Attendance check/Attendance data print Client monitoring | Set | 1 |  |  |
|  | E. Miscellaneous |  |  |  |  |  |
| 1 | UPS | Output Power Capacity: 10 KVA Input - Voltage Range: 90~130AVC - Frequency: 50/60Hz ± 5% - Max Input Current: 112A Output - Voltage Range: 110AVC± 1% - Frequency: 50/60Hz ± 5% - AVR Function: included Battery Type Maintenance-free sealed Lead-Acid battery Typical recharge time: 90% capacity after 8 hours Surge Protection Backup Time: 30 minutes or less Comply with electricity standards of Colombia | Set | 1 |  |  |
| 2 | UPS for PC | Output Capacity: 450Watts / 750 VA Max Configurable Power: 450 Watts / 750 VA Input /Output Voltage: 120V, 50/60Hz ± 3Hz Battery Type: sealed Lead-Acid battery Typical recharge time: 16hour Backup Time at Half Load: 11minute(225 Watts) Comply with electricity standards of Colombia | Set | 31 |  |  |
| 3 | Rack | 19" 42U Aluminum | Set | 1 |  |  |
| 4 | Power & Network Cabling | Network Cabling (35ports): Cat 5 or 5e and miscellaneous materials Power Cabling: HIV 600 heat-resistant Cable and power plugs of Colombian Type Comply with electricity standards of Colombia | Set | 1 |  |  |

- Interior

| No | Equipment | Specification | Unit | Q'ty | Compliance (Y/N) Partially compliant | Bidder’s Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Furniture | Office Desk for Trainees: 30EA Chair: 31EA Printer Desk: 2EA * Reference only and minimum requirements | Set | 1 |  |  |
| 2 | Interior | Wall, Roof, Window, and etc Air Conditioner * The Bidder shall propose a space plan. | Set | 1 |  |  |

# 7) General Classroom

- H/W and S/W

| No | Equipment | Specification | Unit | Q'ty | Compliance (Y/N) Partially compliant | Bidder’s Comments |
| --- | --- | --- | --- | --- | --- | --- |
|  | A. Electronic Desk Board |  |  |  |  |  |
| 1 | PC for Trainer | Processor: Intel core i5-2400 processor(3.10 GHZ,6MB) and above Graphics: 1GB and above Memory: 6GB(DDR3 1333MHZ/4GB +2GB) HDD: 1TB (7200RPM S-ATA2) Monitor: 22" LCD Monitor O/S: Windows 7 Home Premium(64-bit) Keyboard: Spanish and English Mouse: USB Type Including Anti-Virus Program | Set | 1 |  |  |
| 2 | PC for Trainee | Processor: Intel core i5-2400 processor(3.10 GHZ,6MB) and above Graphics: 1GB and above Memory: 6GB(DDR3 1333MHZ/4GB +2GB) HDD: 1TB (7200RPM S-ATA2) Monitor: 22" LCD Monitor O/S: Windows 7 Home Premium(64-bit) Keyboard: Spanish and English Mouse: USB Type Including Anti-Virus Program | Set | 15 |  |  |
| 3 | Multi Function Color Printer | Color Print, Copy, Scan, Fax Printing Print Speed (Black): 21ppm Print Speed (Color): 21ppm Paper Input Capacity (Standard): 250 sheets Copy Copy Speed (Black): 21cpm Copy Speed (Color): 21cpm  Scan Method: Color CCD or CIS or Flatbed Scan Speed(Black): 11ipm or higher Fax Modem Speed (kbps): 33.6 Compatibility: ITU-T G3 Fax Memory: 4MB or up to 250pages General Interface: USB 2.0, Ethernet 10/100 Base TX Memory: 256MB | Set | 2 |  |  |
| 4 | Software | MS-Office, Office University 2010 | Set | 16 |  |  |
| 5 | e-Podium | Type: Stand Type Top unit equipped with a minimum 21” writable LCD Tablet monitor. PC and monitor locking system to prevent theft. Built-in board cable and microphone Including Gooseneck Microphone, content authoring S/W This product shall come form the same manufacturer of the Interactive Display Board. | Set | 1 |  |  |
| 6 | Video Projector and Screen | Projector Native Resolution: XGA (1024x768) Brightness (ANSI-Lumens): 4000ANSI Contrast Ratio (FIFO): 2000:1 and above Lamp life (hours): 2500 and above Screen Size: 120”(2400 x 1800) Material: Matt White Motorized | Set | 1 |  |  |
|  | B. Audio System |  |  |  |  |  |
| 1 | Wireless Microphone | Handheld Transmitter Audio Input Level: +2 dBV maximum at -10dB position Gain Adjustment Range: 10dB RF Transmitter Output: 30mW Maximum Battery Life 8 hours (alkaline) Including Microphone Receiver: XLR connector (into 600 Ω load): –13 dBV XLR Out: Impedence balanced Including external power supply Comply with frequency rate of Colombia | Set | 2 |  |  |
| 2 | Wired Microphone | Type: Dynamic Frequency Response: 50 to 15,000 Hz Polar Pattern: Cardioid Sensitivity: –54.5 dBV/Pa (1.85 mV) | Set | 2 |  |  |
| 3 | DSP Mixer | Acoustical Echo Cancellation Noise Cancellation Built-in telephone interface and 35W power amplication Audio Performance Frequency Response: 20Hz to 22KHz ±1dB Dynamic Range: 105dB(non A-weighted) Matrix Mixing Parameters 12 analog in/out 18 expansion bus in/out 8 assignable processing blocks in/out 4X35W speaker amplication 1 telco input/1 telco out Control 10/100 Mbps Ethernet Network Port and PC Port RS-232(DB-9 female) USB 2.0 compatible Including Configuration and Admin Software | Set | 1 |  |  |
| 4 | Ceiling Speaker | Frequency range (-10 dB): 80 Hz - 20 kHz Power handling (pink noise): 20 W Sensitivity: 86 dB, 1 W @ 1 m, 1/2 space Nominal impedance: 8 Ω | Set | 8 |  |  |
|  | C. Video System |  |  |  |  |  |
| 1 | HD Matrix Switcher | RGBHV+Stereo, 8in 8out RS-232 Control Audio Input Level(max): +14dBu, unbalanced Input Impedence: 18KΩ Output Level(max): +14dBu, unbalanced Output Impedence: 50Ω Connectors: 3T Wideband Video Input Level(max): +/- 1.5V Input Impedence: 75Ω Frequency Response: 300MHz or better(+/- 3dB) HV Sync Input Level(max): +/- 5V HV Sync Output Level(max): +/- 5V Connectors: HD-15 | Set | 1 |  |  |
| 2 | Visual Presenter | Capture area : 420 x 336(mm) Focus : Auto / Manual Camera Module: 42X Zoom, 1,300,000 pixels Input: VGA(15pin D-Sub Output: VGA(15pin D-Sub), DVI Interface: RS-232C, USB, SD Memory | Set | 1 |  |  |
|  | D. Classroom Control |  |  |  |  |  |
| 1 | Controller | 7 Configurable RS-232 / RS-422 / RS-485 Serial ports 8 Relays 8 IR / Serial ports 8 Digital I/O ports 2 Communication Networks: AxLink and Ethernet (TCP/IP) 404 MIPS processor speed 64 MB RAM or 256 MB RAM 2 GB CompactFlash 1 MB Non-Volatile Memory | Set | 1 |  |  |
| 2 | Lecture Touch Control Panel | Compact 4.3" size 16x9 WQVGA color display Screen resolution (HV): 480 x 272 pixels Available in a high-gloss and textured matte combination finish in your choice of black or white Power over Ethernet (PoE) 128 MB Standard memory / 256 MB Flash memory 1 capacitive-touch external button | Set | 1 |  |  |
| 3 | Wireless Touch Panel | Retina display 9.7-inch (diagonal) LED-backlit glossy widescreen Multi-Touch display with IPS technology 30-pin dock connector port 3.5-mm stereo headphone mini jack Built-in speaker Microphone | Set | 1 |  |  |
| 4 | iPad License | Administrators shall be able to control and manage the equipment through iPad. | Set | 1 |  |  |
| 5 | Program Fee | Audio/Visual equipment on/off control Camera Pan/Tilt/Zoom control Signal input/output control through HD Matrix Switcher and DSP Mixer | Set | 1 |  |  |
| 6 | Classroom Management S/W | 1 Teacher and 15 Student License Recovery management function System recovery/Existing status store Reserved recovery set-up Recovery install/delete PC management function Screen lock/unlock Internet lock/unlock Registry lock/unlock Task management lock/unlock Program execution lock/unlock Instruction tool Sending message Sending notice message Remote execution Attendance check/Attendance data print Client monitoring | Set | 1 |  |  |
|  | E. Miscellaneous |  |  |  |  |  |
| 1 | UPS | Output Power Capacity: 10 KVA Input - Voltage Range: 90~130AVC - Frequency: 50/60Hz ± 5% - Max Input Current: 112A Output - Voltage Range: 110AVC± 1% - Frequency: 50/60Hz ± 5% - AVR Function: included Battery Type Maintenance-free sealed Lead-Acid battery Typical recharge time: 90% capacity after 8 hours Surge Protection Backup Time: 30 minutes or less Comply with electricity standards of Colombia | Set | 1 |  |  |
| 2 | UPS for PC | Output Capacity: 450Watts / 750 VA Max Configurable Power: 450 Watts / 750 VA Input /Output Voltage: 120V, 50/60Hz ± 3Hz Battery Type: sealed Lead-Acid battery Typical recharge time: 16hour Backup Time at Half Load: 11minute(225 Watts) Comply with electricity standards of Colombia | Set | 16 |  |  |
| 3 | Rack | 19" 42U Aluminum | Set | 1 |  |  |
| 4 | Power & Network Cabling | Network Cabling(19 Port): Cat 5 or 5e and miscellaneous materials Power Cabling: HIV 600 heat-resistant Cable and power plugs of Colombian Type Comply with electricity standards of Colombia | Set | 1 |  |  |

- Interior

| No | Equipment | Specification | Unit | Q'ty | Compliance (Y/N) Partially compliant | Bidder’s Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Furniture | Office Desk for Trainee: 15EA Chair: 31EA Printer Desk: 2EA * Reference only and minimum requirements | Set | 1 |  |  |
| 2 | Interior | Wall, Roof, Window, etc Air Conditioner * The Bidder shall propose a space plan. | Set | 1 |  |  |

# 8) RIC Security System

- H/D and S/W

| No | Equipment | Specification | Unit | Q'ty | Compliance (Y/N) Partially compliant | Bidder’s Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Camera | Image Sensor: 1/3” CCD Pixels: 410,000 Pixels, 811(H) X 494(V) Horizontal Resolution: 600TV Line(Color), 700TV Line(B/W) Video Out: CVBS: 1.0p_p, Composite S/N Ration: 52dB Minimum Illumination(B/W): 0.01Lux(50IRE@F1.2), 0.00002Lux(Sens-up, x512) OSD: Spanish | Set | 10 |  |  |
| 2 | Motion Detection Sensor | Motion Detection Sensor (8 Set) Sensing Method: Infrared Detection Range: 12m X 1m Mount Type: Ceiling Type Alarm: NC/NO Door Sensor(10Set) Sensing Distance: 25~55mm Installation Location: In the Door or Window Materials: Cover(ABS), Magnet * Required number and kind of equipment may vary depending on the actual space of RIC. | Set | 1 |  |  |
| 3 | DVR | Video Input: Composite 16CH Monitor Output - Main Composite; BNC, 1 Vp-p, 75 ohm - VGA: 800X600, 1024X768, 1280X1024 - HDMI: 480P/720P/1080P(1920X1080) Audio: 16CH In/1CH Out Recoding - Compression: H.264 - Resolution: up to 480FPS @ 704X480 Searching: Date/time, Event, Back up, Pos, Motion (*All Search Included Prview Function) Alarm in/out: 16 line in / 4 relay out HDD: 1TB Network - Network: 10/100/1000Mbps - USB 2.0: 3 Ports - Web Viewer Function PTZ Control:RS-485 Serial Interface: RS-232 including 17” Monitor | Set | 1 |  |  |
| 4 | UPS | Output Power Capacity: 5 KVA Input - Voltage Range: 100 ~ 280V - Frequency: 50/60Hz ± 5% Output - Voltage Range: 120V - Frequency: 50/60Hz ± 3Hz Battery Type Maintenance-free sealed Lead-Acid battery Typical recharge time: 2.5 hours Surge Protection and Filtering: Included Backup Time: 18 minutes(at 1,750Watts) or more Comply with electricity standards of Colombia | Set | 1 |  |  |
| 5 | Rack | 19", 22U Aluminum | Set | 1 |  |  |

# 3. Lab School

-H/W and S/W

| No | Equipment | Specification | Unit | Q'ty | Compliance (Y/N) Partially compliant | Bidder’s Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | F/W | Anti-Virus Child Protection 1Year License for Server | Set | 50 |  |  |
| 2 | Network Switch | Ports: 22 autosensing 10/100/1000 ports or more Mounting: EIA-standard 19" Rack Memory and processor: 8 MB flash, packet buffer size: 512 KB, 16 MB SDRAM Throughput: up to 35.7 million pps (64-byte packets) Management features: Web browser Switching capacity: 48 Gbps | Set | 50 |  |  |
| 3 | Proxy Server | OS: WIndows7 Professional 64 Processor: Intel Xeon Quad-Core W3520(2.66GHz, 8MB cache, 1066Mhz Memory) * 1EA Memory: 4GB DDR3 HDD: 500GB 7200rpm SATA Optical Drive: SATA Super Multi-DVD Writer Graphic Memory: 512MB Network: 10/100/1000Mbps Keyboard and Mouse including 22" LCD Monitor | Set | 50 |  |  |
| 4 | Access Point (WiFi) | 802.11a/b/g, 54Mbps Dual Antenna Authentication: Security Standards, WPA, WPA2 (802.11i) Encryption: AES encryption (WPA2), TKIP (WPA), WPA TKIP | Set | 300 |  |  |
| 5 | Notebook | OS: Windows7 Home Premium (64bit) CPU: Intel Core i5 Processor 3210M, 2.60Ghz, 3MB or higher Screen Size: 15.6" Resolution: 1366 X 768 Memory: 6GB DDR3 HDD: 500GB ODD: DVD +/- RW Speakers: Stereo Speaker Web Camera: HD Camera Connectivity: 802.11 b/g/n, Gigabit Wired Ethernet LAN, Bluetooth Keyboard: 101 Key(Spanish or English) Touch Pad Including AC Adapter, Optical USB Mouse, Anti-Virus S/W | Set | 1100 |  |  |
| 6 | Software | MS-Office , Home and Student | Set | 1100 |  |  |
| 7 | Multi Function Printer | Color Print, Copy, Scan Printing Print Speed (Black): 17ppm or higher Print Speed (Color): 4ppm Copy Copy Speed (Black): 17cpm or higher Copy Speed (Color): 4ppm Scan Method: Color CIS or CCD or Flatbed Resolution (Optical): up to 1200dpi or higher Scan Speed: up to 14ppm General Interface: High-Speed USB 2.0 / 10/100 Base Tx / Wireless 802.11 b/g/n Memory: 128MB | Set | 100 |  |  |
| 8 | Toner | Toner for Multifunction Color Printer(Black): 300EA Toner for Multifunction Color Printer(Yellow): 300EA Toner for Multifunction Color Printer(Magenta): 300EA Toner for Multifunction Color Printer(Cyan): 300EA | Set | 1 |  |  |
| 9 | Projector and Portable Screen | Projector Native Resolution: XGA(1024x768) Brightness(ANSI-Lumens): 3200ANSI Contrast Ratio(FIFO): 2000:1 and above Lamp life(hours): 3000 and above Portable Screen Size: 120”(2400 x 1800) Material: Matt White | Set | 100 |  |  |
| 10 | Portable Station | Enough storage to accommodate 11 or more notebooks Portable interface Charging system Security lock | Set | 100 |  |  |
| 11 | UPS | Capacity: 3000VA Output Voltage: 120V Output Frequency: 50 or 60Hz +/-10% Voltage Regulation( AVR) function Input Voltage: 120V Input Frequency: 50 or 60Hz +/-3% Battery type: Sealed, maintenance-free lead acid batteries with 3-6 years typical lifetime Back-up Time(a PC with 15" monitor): 95~105 mins * Comply with electricity standards of Colombia | Set | 50 |  |  |
| 12 | Power Extension | 6 Socket 3M * Comply with electricity standards of Colombia | Set | 200 |  |  |
| 13 | Classroom Management S/W | 2 Teacher License, 20 Student License Recovery management function System recovery/Existing status store Reserved recovery set-up Recovery install/delete PC management function Screen lock/unlock Internet lock/unlock Registry lock/unlock Task management lock/unlock Program execution lock/unlock Instruction tool Sending message Sending notice message Remote execution Attendance check/Attendance data print Client monitoring | Set | 50 |  |  |